## Slide 1
Adaptive Smart Room
Occupancy & Energy Controller
A reproducible Soft Computing minor project
Genetic Algorithm · Mamdani fuzzy logic · Energy simulation
Seven phases, one explainable pipeline.
Academic prototype; no devices are actuated.
Notes: Introduce the goal: infer room occupancy, explain control requests, and estimate energy under stated assumptions. The dataset contains no measured electricity labels. Source: UCI Room Occupancy Estimation, https://doi.org/10.24432/C5P605

## Slide 2
From sensor readings to an explainable request
Sensors → occupancy model → fuzzy controller
→ energy policy → simulated power and energy
GA selects estimator inputs during development.
The dashboard runs saved models; it never retrains them.
Notes: Explain that GA is offline feature selection, not a component run on every reading. Fuzzy inputs are predicted occupancy, S1 temperature, S1 light and S5 CO2. Sources: src/occupancy_system.py, src/fuzzy_controller.py, src/energy_controller.py.

## Slide 3
The dataset needs a chronological evaluation
10,129 observations · 19 original columns
Occupancy classes: 0, 1, 2 and 3 people
81.23% of rows describe an empty room
Train: Dec 22 · Validation: Dec 23 · Later test: Dec 24 onward
Ten-minute boundary embargo; recording gaps are retained.
Notes: The empty-class fraction is 8228/10129 = 81.23%. No missing values or duplicate timestamps were found. Raw data are preserved and all rows retained. Aggregates were created for exploration; direct sensor channels form the baseline. Source: outputs/tables and docs/phase2_protocol.json.

## Slide 4
High accuracy hides occupied-room failures
Baseline validation macro F1: 0.8608
Later-test accuracy: 95.32%
Later-test balanced accuracy: only 38.99%
Always-empty test accuracy: 94.99%.
Both models misclassify 184 of 294 occupied test rows as empty.
Notes: Explain class imbalance using the always-empty classifier. Class 1 is absent in the later test, so test balanced accuracy concerns three present classes. The test data were already examined and are not a new blind test. Source: outputs/phase4/tables/professor_comparison.csv and occupancy_error_analysis.csv.

## Slide 5
GA trades input count against prediction quality
15 binary genes → 4 selected inputs
S1_Light · S5_CO2 · S6_PIR · S7_PIR
Fitness = training macro F1 − 0.05 × selected / 15
73.33% fewer estimator inputs.
Validation macro F1 falls from 0.8608 to 0.7952.
Notes: Describe population 16, tournament selection, one-point crossover, bit mutation, 10 generations and 3 seeds. Fitness uses purged within-training-day blocks; this tests interpolation, not forecasting. The complete controller also needs S1_Temp, giving five channels. Baseline stays the default. Sources: docs/phase3_notes.md, models/phase3/selection_locked.json.

## Slide 6
Fuzzy logic makes the control request inspectable
34 rules · minimum AND · maximum aggregation
Centroid defuzzification → lighting and ventilation %
Example: high occupancy + dark room → high lighting.
Poor CO₂ quality → high ventilation, even if occupancy is zero.
Notes: Explain membership degrees versus probability. The fuzzy rules map gradual conditions to gradual requests. A fuzzy off set has a positive centroid; a separate zero-occupancy gate makes lighting exactly zero. Membership thresholds are illustrative project assumptions, not health or ventilation standards. Source: config/phase5_fuzzy.json.

## Slide 7
Energy results depend on explicit assumptions
Assumed full loads: lighting 60 W + ventilation 40 W
Energy (kWh) = power (W) × duration (s) / 3,600,000
ECO · NORMAL · COMFORT · deterministic AUTO
Integrate only short recorded intervals within one partition.
Exclude gaps, embargo crossings and unknown final durations.
Notes: AUTO uses CO2, occupancy and temperature thresholds; adaptive means rule-based response, not online learning. Requests scale power linearly. No HVAC, standby, controller or sensor power is included. Source: config/phase6_energy.json and docs/phase6_notes.md.

## Slide 8
Apparent energy reduction is not proof of success
Later-test AUTO: 0.147 kWh simulated
Full-power comparator: 4.930 kWh
Covered test duration: 49.30 hours
But lighting is zero for 1.55 of 2.48 occupied hours.
Do not claim 97% measured savings or equivalent comfort.
Notes: Both models have identical AUTO energy on the test replay because their remaining differences fall in the same high-occupancy fuzzy region. The true-label reference uses known labels and is not deployable or optimal. Source: outputs/phase6/tables/energy_summary.csv, test AUTO rows.

## Slide 9
Demonstrate the reasoning, then the limitation
1 Empty + dark → exact lighting off
2 High occupancy + high CO₂ → high requests
3 Low occupancy + bright → low lighting
4 Recorded false-empty → explain the failure
Open the fired rules and membership degrees.
Compare energy estimates with occupied zero-light hours.
Notes: Use dashboard manual mode for the three teaching scenarios: it bypasses the classifier. Then use GA or baseline with later-test example 1, whose actual occupancy is three but the model predicts zero. Explain the distinction between an implementation test and predictive reliability.

## Slide 10
A complete prototype, with a clear next experiment
Delivered: raw data, models, GA search, fuzzy rules,
energy replay, local dashboard and reproducible checks.
Next: collect new rooms and occupied examples, improve recall,
add temporal safeguards, and measure actual load and comfort.
Notes: Conclude: the contribution is an integrated, explainable academic system with transparent evaluation. It is not a validated building controller. Run src/verify_phase7.py for integration checks. Read docs/phase7_notes.md and docs/presentation_guide.md for the complete demo and limitations.